## Slide 1: Design Credit Presentation
Indian Institute of Technology, Jodhpur
Project - Modulation of Variable Transformer using Arduino for constant Power output
Nikhil Gangwar(B20ME049)
Faculty Supervisor - Dr. Sudipto Mukhopadhyay

## Slide 2: Our Aim for the project
AC Variac
Stepper Motor
Current Sensor
Voltage Sensor

## Slide 3: Device Architecture
VARIAC CONTROL
Based on continuously feeding data from sensors we repeat steps 3 and 4 to control variac
STEP-5
DRIVER AND CONTROL CIRCUIT
After taking decision we direct our stepper motor via dedicated drivers
STEP-4
MICROCONTROLLER
Taking readings from voltage and current sensor we decide how to control device
STEP-3
GIVING USER INPUT
Using Keypad we give required power input to the device
STEP-2
RESETTING
When the device starts we bring the variac to its initial position with the help of Limit switches
STEP-1

## Slide 4: Our Device

## Slide 5: Code Part
My major contribution was in the controlling of Voltage sensor ZMPT101b and taking input via keypad

## Slide 6: Future Scope
The current sensor ACS712 is a current sensor but it sometimes shows incorrect data so in order to increase the accuracy we can use a different sensor named SCT013. It is more expensive but due to a bigger coil provides more accuracy
Plus this device can be upgraded into an IOT based device where a researcher can setup the device and can monitor the status via his/her smartphone over a bluetooth or wifi connection using an ESP32 chip

## Slide 7
List of Components Used
COMPONENTS | USES
Arduino Mega | To connect all the hardware components
ZMPT101B | To measure variac voltage
ACS712 | To measure variac current
Nema 17 Stepper Motor | To rotate variac shaft
Led Display | To display input and output
Keypad | To take user input
Me and Somil Maheshwari who are doing this project collectively are currently working on drafting a proper paper for the given device.
https://docs.google.com/document/d/19eu0ZI07kGT_iH85_kBw5iDBFLcigjXXyNTyQ8cGZp0/edit?hl=en&forcehl=1

## Slide 8: Thank You